## Slide 1: Research on DC electric source characteristics
Artur Abdullin, Konstantin Gorshkov, Sergey Lovlin
Faculty of Control Systems and Industrial Robotics, ITMO University, Saint Petersburg

## Slide 2: Contents
Objectives
Program of work
Basic theory
Guidance
Content of the report
Special tasks

## Slide 3: Objectives
  to study operating modes of electrical energy sources: open circuit, short-circuit and maximum power transfer;
  to study the procedure of experimental determination of the electrical energy source equivalent circuit parameters;
  to study the maximum power transfer theorem and Thevenin's theorem.
  to learn how to use LTspice software for circuit analysis;

## Slide 4: Program of work
  plot the volt-ampere characteristic of real voltage source;
  identify the parameters of the equivalent circuit for real electrical source based on experimental data.
  simulate the circuit by LTspice;

## Slide 5: LTspice
  LTspice – is freeware version of SPICE provided by Linear Technology.
  SPICE ("Simulation Program with Integrated Circuit Emphasis") - analog electronic circuit simulator.
  First version of SPICE was developed at the Electronics Research Laboratory of the University of California, Berkeley in 1973.

## Slide 6: Task
  Given that E1=10 [V], E2=20 [V], R1=100 [Ω], R2=200 [Ω]
  and R3=200 [Ω], find the currents.

## Slide 7: Thevenin's theorem (1883)
  Any linear electrical network containing only one-ports can be replaced at terminals a-b by an equivalent combination of a voltage source Eth in a series connection with a resistance Rth.

## Slide 8: Thevenin's theorem (1883)
  Any linear electrical network containing only one-ports can be replaced at terminals a-b by an equivalent combination of a voltage source Eth in a series connection with a resistance Rth.

## Slide 9: Maximum power transfer
  The maximum power transfer theorem was developed by Moritz Hermann von Jacobi, a German and Russian engineer and physicist, around 1840.

## Slide 10: Guidance
  Open your circuit model of the real voltage source in LTspice;
  Measure open circuit voltage U0 and put the result in the Table 1.1.;
  By changing load resistance determine its value which provides voltage in the load equal to U0/2. Enter determined value in the table as r;
  By varying load resistance from 0 [Ω] to 10000 [Ω] accordingly to the Table 1.1, obtain corresponding values of voltage, current and power dissipated in load, and put them into the Table 1.1.
  Open file EE_Lab1.pdf;

## Slide 11: Guidance
  For each pair of current values and voltages for k = 2...10 calculate and put in the Table 1.1 source internal resistance rk [Ω];
  Find an estimate of the source's internal resistance r as a root mean square value;

## Slide 12: Guidance
  Calculate the short-circuit current of the source Isc = U0/r;
  Calculate the efficiency ηk = Rnk/(r + Rnk);
  Draw a line on the plot through points [0, E = U0] and [Isc, 0] which will be the calculated volt-ampere characteristic of source and show points of the experimental characteristic according to the Table 1.1. on the same plot.
  According to the Table 1.1, build power dependencies of load and efficiency.

## Slide 13: Table 1.1.

## Slide 14: Content of the report
  1. The equivalent circuit.
  2. Filled Table 1.1.
  3. Plot of the calculated and experimental characteristic of the source.
  4. Dependency diagrams for Pn(In) and η(In).

## Slide 15: Special tasks
  Task 1. Use Thevenin's theorem to find Eth and Rth.
  Task 2. Use equivalent transformations to find Eeq and Req.